|  | Configuration of Permanent Magnet Electric Motor |
| --- | --- |
|  | 5KW Brushless DC Motor |
| NO. | Parmeters | Units | Amount | Remark |
| 1 | Rated Power | kW | 5 |  |
| 2 | Peak Power | kW | 10 | Limiting the specific values of the secision by the controller |
| 3 | Rated Voltage | VDC | 72 |  |
| 4 | Rated Current | A | 80 |  |
| 5 | Rated Torque | Nm | 17 |  |
| 6 | Overload Torque | Nm | 50 | Limiting the specific values of the secision by the controller |
| 7 | Rated Speed | rpm | 2800 |  |
| 8 | Max. Speed | rpm | 3400 |  |
| 9 | Anti-Electromotive | V/rad·s-1 | 0.17 |  |
| 10 | Phase Current Average | A | 106 |  |
| 11 | Working Type |  | 1h |  |
| 12 | Protection Grade |  | IP55 |  |
| 13 | Insulation Level |  | F |  |
| 14 | Cooling Mode |  | AIR |  |
| 15 | Frame |  | Y112-B35 |  |
| 16 | Weight | kg | 25 |  |
| 17 | Appearance |  |  |  |
|  |  | Practical requirements of motor output shaft can be customized |
| 18 | Size | mm | Φ184×L297MM |  |
| CONTROLLER SPECS. | BSC15-72 |
| INPUT VOLTAGE RANGE 18-88V COOLONG TYPE AIR |
| MAX OUTPUT CURRENT 300A WORKING TEMPERATURE -20-60 |
|  |  | SIZE 200X146X62MM |
| KEEP TEMPERATURE -30-80 WEIGHT 2.5 KG |

| PEDAL |
| --- |
| INPUT VOLTAGE | 0.8--4.2V |
| CONTROL TYPE | POTENTIONMETER |
| INPUT VBOLTAGE | 5v |
| Resister | 10k |